## Slide 1: What land cover characteristics drive trends in surface water quality?
Nick Lamkey
nclamkey@gmail.com

## Slide 2
Mine remote sensing data to look for predicters of nitrate concentrations
Remote Sensing Data
  NDVI
  Evapotranspiration
  Crop land data layer
  Land use land cover
  DEM
  Temperature
  Precipitation
Use high resolution in-situ nitrate-nitrite and discharge data to characterize nitrate flux and behavior in streams
Goal

## Slide 3: Why is this important?
Human Health Concerns
The EPA set a 10 mg/l maximum contaminant level for nitrate to protect against blue baby syndrome
It is unknown if nitrate above 10 mg/l is harmful to adults
Environmental Health Concerns
Causes hypoxic conditions in water bodies that accumulate nitrates, which kill aquatic life
Every year, one of the world's largest hypoxic zones develops in the Gulf of Mexico primarily as a result of agricultural runoff from the Midwest

## Slide 4: What to do with the data?
Use a method that considers all the remote sensing data at the same time to define a region that is most likely impacting nitrate levels at the in-situ measuring point
Use the defined region to start looking for trends that may be related to nitrate behavior in streams and potentially groundwater adjacent to streams

## Slide 6: K-means Clustering
K-means clustering is a type of unsupervised machine learning used to find groups in the data
Compiled 370 layers of NDVI, ET, CDL, LUCL, Precip., and Temp data into a single data cube
Ran several iterations of k-means clustering and landed on 6 groups of data

## Slide 7: Start characterizing the region influencing the in-situ nitrate-nitrite sensor

## Slide 10: In-situ nitrate-nitrite data
Plot from Baker and Showers (2018)
Hysteresis Loops
Counter-clockwise suggests a delayed response where nitrates could be coming from upstream or subsurface flow
Clockwise which suggests rapid solute input from storm events

## Slide 11: Hysteresis Loops

## Slide 12: Next Steps
Use the events defined in the hysteresis loops to associate data from the cluster analysis to the response of nitrate values in the stream
Refine k-means clustering analysis
  smaller cell sizes
  eliminate more data with NAN values
  add a soils map and other available data
Refine workflow for finding events that create hysteresis loops
Try c-means fuzzy clustering
Try a supervised classification
Use streamstats to delineate the drainage to the in-situ point